## Slide 1: Industrial Applications
Product Line Industrial Filtration Technology
Status: March 2012
Product Training

## Slide 2: Content
Central Applications
Air Quality – air for general purpose
Air for high quality purpose
Air for Critical Applications
Filter performance overview

## Slide 3: Content
Central Applications
Air Quality – air for general purpose
Air for high quality purpose
Air for Critical Applications
Filter performance overview

## Slide 4: Industrial Applications
Central Application
Compressor Room
De-Central Application
(POU = Point of Use)
Laser Technology
Breathing Air
Paint Shop
Process Air
…??? Application
Basic purification
POU or special purification

## Slide 5: Industrial Applications
Central Application
Basic purification requirements depending on application conditions:
Compressed Air Generation
Oil- lubricated
Oil-free
Compressed Air Capacity
Volume flow
Ambient Conditions
Temperature >+3ºC
Temperature ≤+3ºC
Operating Conditions
Pressure
Temperature
Customer specific requirements

## Slide 6: Industrial Applications
Selection criteria for air purification products
Air Flow
Filters/Separators: DF, AG, SG?
Dryers: Buran, Boreas, Brisa?
Air Temperature
After-cooler UFK-W / UFK-L needed?
Air Receiver Vessel?
Pollutions
Oil aerosol + oil vapor?
Liquid water or aerosols + water vapor?
Solid particles?
Air Quality
General purpose?
High quality?
Critical or special applications?
Other pollutions (CO2, CnHn, etc.)
Dryers: UP 2000, Classic, Dryer Systems?

## Slide 7: Industrial Applications
What about „oil-free“ generated air?
SO2
NH3
CO
CO2
O3
VOC
NOX
H2O
Particles
SO2
NH3
CO
CO2
O3
VOC
NOX
CO2
NH3
NOX
VOC
VOC
Compressed Air
Compressor
Atmospheric Air
Even „oli-free“ generated air needs purification
Water separators + filters (downstream coolers)
Dryers (removal of water vapor)
Activated carbon adsorbers / filters (removal of contaminants of ambient air)

## Slide 8: Content
Central Applications
Air Quality – air for general purpose
Air for high quality purpose
Air for Critical Applications
Filter performance overview

## Slide 9: Industrial Applications
Air Quality
Recommended Quality Classes acc. to VDMA 15390:2012 (Draft)
(German Engineering Federation)
Application | Solid particles | Water (vapor) Tamb >3ºC | Water (vapor) Tamb ≤3ºC | Total oil
Control air for oil/gas drilling | 7 | 4 | 2-3 | 4
Mining tools (pneumatic drill) | 7 | 4 | 2-3 | 4
Pneumatic drive (actuators) | 2 | 4 | 2-3 | 2
Air blast (mould tools, air guns) | 2-3 | 4 | 2-3 | 2
Pre-purified air to point of use applications | 2-3 | 4 | 2-3 | 2-3
Control air for industrial applications | 2-3 | 4 | 2-3 | 2
Transport air for industrial applications | 3 | 4 | 2-3 | 2
Air for general purpose

## Slide 10: Industrial Applications
Central application with oil-lubricated compressor
Volume flow < 1100 m³/h
Ambient temperature (Tamb) 15ºC…25ºC
Compressor with integrated air-cooled cooler (Tout ≈ Tamb+10K)
Air receiver vessel downstream compressor (optional)
Air for general purpose (Solution 1)
DF-C
DF-V
DF-M
Pre filter required upstream fridge dryer – protection of heat-exchanger

## Slide 11: Industrial Applications
Air for general purpose (Solution 1)
DF-C
DF-V
DF-M
Solid Particles
Water Vapor
Total Oil
7
7
5
6
7
4
4
7
3
4
4
3
2
4
2

## Slide 12: Industrial Applications
Central application with oil-lubricated compressor
Volume flow < 1100 m³/h
Ambient temperature (Tamb) 15ºC…25ºC
Compressor with integrated air-cooled cooler (Tout ≈ Tamb+10K)
Air receiver vessel downstream compressor (optional)
Air for general purpose (Solution 2)
DF-P
Pre filter P required to remove big particles and water/oil aerosols
DF-M

## Slide 13: Industrial Applications
Air for general purpose (Solution 2)
DF-P
DF-M
Solid Particles
Water Vapor
Total Oil
7
7
5
7
7
4
2
7
2
2
4
2
2
4
2
Oil aerosols could be present after fridge dryer!

## Slide 14: Industrial Applications
Central application with oil-lubricated compressor
Volume flow < 1100 m³/h
Ambient temperature (Tamb) -10ºC…25ºC
Compressor with integrated air-cooled cooler (Tout ≈ Tamb+10K)
Air receiver vessel downstream compressor (optional)
Air for general purpose (Solution 3)
DF-C
DF-V
Dustfilter DF-M required to achieve particle Class 2
Optional
Adsorption dryer required for pressure dewpoint < -10ºC
HED/ALD
DF-M

## Slide 15: Industrial Applications
Air for general purpose (Solution 3)
DF-C
DF-V
Optional
HED/ALD
Solid Particles
Water Vapor
Total Oil
7
7
5
6
7
4
4
7
3
4
4
3
5
2
2-3
DF-M
2
2
2-3

## Slide 16: Content
Central Applications
Air Quality – air for general purpose
Air for high quality purpose
Air for Critical Applications
Filter performance overview

## Slide 17: Industrial Applications
Air Quality
Recommended Quality Classes acc. to VDMA 15390:2012 (Draft)
Application | Solid particles | Water (vapor) Tamb >3ºC | Water (vapor) Tamb ≤3ºC | Total oil
Pre-purification for process air (Pharmaceutical, food + beverage industries) | 2 | 3-4 | 1-3 | 1
Blow moulding of plastics | 1 | 4 | 2-3 | 1
Instrument or blowing air for semiconductor industry | 1 | 1-2 | 1-2 | 1
Measurement and test technology | 1 | 4 | 1-3 | 1
Transport air for process applications | 1-2 | 4 | 2-3 | 1-2
Air for high quality purpose

## Slide 18: Industrial Applications
Central application with oil-lubricated compressor
Volume flow < 1100 m³/h
Ambient temperature (Tamb) -10ºC…25ºC
Compressor with integrated air-cooled cooler (Tout ≈ Tamb+10K)
Air receiver vessel downstream compressor (optional)
Air for high quality purpose (Solution 1)
DF-C
DF-V
Cyclone separator required to remove liquid water during cold period
Optional
MSD
Pre filter required upstream fridge dryer – protection of heat-exchanger
DF-A

## Slide 19: Industrial Applications
Air for high quality purpose (Solution 1)
DF-C
DF-V
Optional
MSD
DF-A
Solid Particles
Water Vapor
Total Oil
7
7
5
6
7
4
4
7
3
4
4
3
5
2
1-2
1
1
1-2

## Slide 20: Industrial Applications
Central application with oil-lubricated compressor
Volume flow < 1100 m³/h
Ambient temperature (Tamb) -10ºC…25ºC
Compressor with integrated air-cooled cooler (Tout ≈ Tamb+10K)
Air receiver vessel downstream compressor (optional)
Air for high quality purpose (Solution 2)
DF-C
DF-V
Optional
MSD
AKC provides extended activated carbon lifetime
DF-Combi
V + S
AKC
Additional dust filter(s) required downstream AKC

## Slide 21: Industrial Applications
Air for high quality purpose (Solution 2)
DF-C
DF-V
Optional
MSD
DF-Combi
V + S
AKC
Solid Particles
Water Vapor
Total Oil
7
7
5
6
7
4
4
7
3
4
4
3
5
2
1-2
5-7
1
1-2
1
1
1-2

## Slide 22: Industrial Applications
Central application with oil-lubricated compressor
Volume flow < 1100 m³/h
Ambient temperature (Tamb) -10ºC…25ºC
Compressor with integrated air-cooled cooler (Tout ≈ Tamb+10K)
Air receiver vessel downstream compressor (optional)
Air for high quality purpose (Solution 3)
DF-C
(Optional)
DF-V
(Optional)
Optional
OFP
OFP provides extended activated carbon lifetime
Additional dust filter(s) required downstream OFP if particle Class 1 is required
DF-S

## Slide 23: Industrial Applications
Air for high quality purpose (Solution 3)
DF-C
(Optional)
DF-V
(Optional)
Optional
OFP
DF-S
Solid Particles
Water Vapor
Total Oil
7
7
5
6
7
4
4
7
3
4
4
3
3
1
1-2
1
1
1-2

## Slide 24: Content
Central Applications
Air Quality – air for general purpose
Air for high quality purpose
Air for Critical Applications
Filter performance overview

## Slide 25: Industrial Applications
Air Quality
Recommended Quality Classes acc. to VDMA 15390:2012 (Draft)
Application | Solid particles | Water (vapor) Tamb >3ºC | Water (vapor) Tamb ≤3ºC | Total oil
Breathing Air (DIN EN12021 + DIN EN ISO 7396-1) | 2 | 3-4 | 2 | 1
Laser applications | 1-2 | 1-3 | 1-3 | 1
Painting + surface refinement (Silicone-free) | 1-2 | 4 | 2-3 | 1
Process air for point of use applications | 1-2 | 1-2 | 1-2 | 1
Extreme conditions (Heavy duty, outdoor) | 1-3 | 1-3 | 1-3 | 1-2
Air for Critical Applications

## Slide 26: Industrial Applications
Breathing air applications
Contaminant | Required Quality EN12021 (Respiratory protective devices) | Required Quality ISO7396-1 (Medical air)
Particles | Not specified (as low as possible) | Class 2 (ISO8573-1:2001)
Water | PDP ≥ 5ºC below min. ambient temperatue | 67 ppm or 870 ppm
Oil (liquid + vapor) | ≤ 0,5 mg/m³ (EN12021) | ≤ 0,1 mg/m³
CO | ≤ 15 ppm | ≤ 5 ppm
CO2 | ≤ 500 ppm | ≤ 500 ppm
SO2 | Not specified | ≤ 1 ppm
NOX | Not specified | ≤ 2 ppm
These contaminants can only be removed by breathing air systems Ultrapure ALG-S or Ultrapure/Medipac2000

## Slide 27: Industrial Applications
Breathing air applications
Central Purification
and…
CO ≤ 5 ppm
CO2 ≤ 500 ppm
SO2 ≤ 1 ppm
NOX ≤ 2 ppm
Solid Particles
Water Vapor
Total Oil
2
4
4-5
2
3
Solution 1:
4
DF-T
DF-V
1
1
4
Pressure regulator
Humidifier

## Slide 28: Industrial Applications
Breathing air applications
Central Purification
and…
CO ≤ 5 ppm
CO2 ≤ 500 ppm
SO2 ≤ 1 ppm
NOX ≤ 2 ppm
Solid Particles
Water Vapor
Total Oil
2
4
4-5
1
2
Solution 2:
4
DF-A
DF-S
1
1
4
Pressure regulator
Humidifier
2
3
4
DF-V

## Slide 29: Industrial Applications
Breathing air applications
Central Purification
and…
CO ≤ 5 ppm
CO2 ≤ 500 ppm
SO2 ≤ 1 ppm
NOX ≤ 2 ppm
Solid Particles
Water Vapor
Total Oil
2
4
2
2
Solution 3: ALG20
4
1
2
4
Humidifier
1
1
4
DF-S
DF-M
DF-A
4-5

## Slide 30: Industrial Applications
Laser applications
Cutting gas
Purging gas
Application | Solid particles | Water (vapor) Tamb >3ºC | Water (vapor) Tamb ≤3ºC | Total oil
Laser applications | 1-2 | 1-3 | 1-3 | 1
For some purge gas application further required:
CO2 content as low as possible
< 100 ppm minimum requirement
< 50 ppm target

## Slide 31: Industrial Applications
Laser applications
Central Purification without adsorption dryer
Solid Particles
Water Vapor
Total Oil
2
4
2
5
1-2
2
1
1
UP2000
DF-A or
DF-T
Solution 1:
UP2000 provide also CO2 reduction
Size as big as possible for most efficient CO2 reduction
1-2

## Slide 32: Industrial Applications
Laser applications
Central Purification without adsorption dryer
Solid Particles
Water Vapor
Total Oil
2
4
2
3
1
1
1
OFP2000
DF-S
Solution 2:
OFP2000 provide also CO2 reduction
Size as big as possible for most efficient CO2 reduction
1-2
1-2

## Slide 33: Industrial Applications
Laser applications
Central Purification with adsorption dryer
Solid Particles
Water Vapor
Total Oil
2
1-2
2
1
1
Solution 3:
No CO2 reduction!
If CO2 reduction is required, install UP2000 upstream
1-2
DF-A or
DF-T

## Slide 34: Industrial Applications
Laser applications
OEM solution
No central Purification
Solid Particles
Water Vapor
Total Oil
6
7
4
2-3
1
1-2
7
7
5
2
7
2
DF-C
DF-M
OFP2000
+
FFP

## Slide 35: Industrial Applications
Painting applications
Application | Solid particles | Water (vapor) Tamb >3ºC | Water (vapor) Tamb ≤3ºC | Total oil
Painting + surface refinement (Silicone-free) | 1-2 | 4 | 2-3 | 1
For painting applications further required:
Free of silicone and parting agent (DE: „labs-frei“)
Filters and dryers must be ordered with special item numbers (specification 0024)
All components free of silicone and specially cleaned (free of oil + grease)
Workers must wear gloves during assembly of housings and filter elements
Special packing (welded plastic bag) for elements

## Slide 36: Industrial Applications
Painting applications
Use air for high quality solutions…
DF-C
DF-V
Optional
MSD
DF-A
DF-C
DF-V
Optional
MSD
DF-Combi
V + S
AKC
DF-C
(Optional)
DF-V
(Optional)
Optional
OFP
DF-S

## Slide 37: Industrial Applications
Industrial air for process applications
Application | Solid particles | Water (vapor) Tamb >3ºC | Water (vapor) Tamb ≤3ºC | Total oil
Process air for point of use applications | 1-2 | 1-2 | 1-2 | 1
Clearly define interface between industrial air (not sterile) and process air (sterile).
Industrial Air
Process Air (sterile)

## Slide 38: Industrial Applications
Industrial air for process applications
Use air for high quality solutions…
DF-C
DF-V
Optional
MSD
DF-A
DF-C
DF-V
Optional
MSD
DF-Combi
V + S
AKC
DF-C
(Optional)
DF-V
(Optional)
Optional
OFP
DF-S

## Slide 39: Industrial Applications
Heavy duty / outddor applications
Application | Solid particles | Water (vapor) Tamb >3ºC | Water (vapor) Tamb ≤3ºC | Total oil
Extreme conditions (Heavy duty, outdoor) | 1-3 | 1-3 | 1-3 | 1-2
ATEX applications
Extremely low ambient temperature
Mobile applications
Please contact product line for special solutions!

## Slide 40: Industrial Applications
Heavy duty / outddor applications
DF filter in dust ambient – ATEX solution required
Filters and dryers must be ordered with special item numbers (specification 0031)

## Slide 41: Industrial Applications
Heavy duty / outddor applications
Ultrapac 2000 in cement plant – ATEX solution required

## Slide 42: Industrial Applications
Heavy duty / outddor applications
T ambient < -50°C
PDP <-75ºC
Fridge dryer for summer period
Classic dryer for summer + winter period

## Slide 43: Content
Central Applications
Air Quality – air for general purpose
Air for high quality purpose
Air for Critical Applications
Filter performance overview

## Slide 44: Industrial Applications
Filter performance overview
Filter Grade | Oil Aerosol Efficiency (ISO12500-1) | Achievable Quality Class for particles | Achievable Quality Class for total oil
C | - | Class 6 | Class 4 - 5
P / PE | 90% | Class 7 (25µm) | Class 4
S / SB | - | Class 7 (25µm) | -
V | 96% | Class 4 - 5 | Class 3
FF | 99% | Class 3 | Class 2 - 3
M / MF | 99,7% | Class 2 (Pre filtration required) | Class 2
S / SMF | 99,8% | Class 1 (Pre filtration required) | Class 2
A / AK | - | Class 1 | Class 1 (Pre filtration required)
T | 99,8% | Class 1 | Class 1

## Slide 45: Questions ?